## Slide 1
IP fabric architecture for grnet Automating the DATACENTER
June 13, 2018, TNC18: Trondheim
Christos Argyropoulos
cargious@noc.grnet.gr
GRNET

## Slide 2
The problem
2
Expanding from
  Two small DCs
  One larger one: 22 racks
To three new datacenters
  Athens: 36 racks (with the expansion)
  Knossos: 26 racks
  Louros: 14 racks
Network architecture?
  Address existing problems
  Balance between already tested and more innovative solutions
  Satisfy new requirement: VLAN stretch between datacenters
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters

## Slide 3
Typical GRNET DC Rack
3
Virtual Machines Lane
Debian, KVM, Ganeti, okeanos/vima
No routing protocols between hosts & network. Simple linux bridging or ARP proxying
Storage Lane
Distributed Object Storage: Debian, Ceph/RADOS
Networking Lane
Also:
Traditional SAN/NAS
Baremetal servers or Colocated third party servers
Monitoring stations, PDUs, TS, …
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters

## Slide 4
GRNET DC Network
4
Single switching fabric across the entire datacenter
VLANs stretching
DC router(s)
  Intervlan routing
  Routing with GRNET IP core
  Firewalling
Server Connectivity
  Active/Active (LACP)
  Active/Backup
  Single homed
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
DC Network
GRNET Core

## Slide 5
Previous Architectures: Ethernet + IP
5
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
Core Router A
Core Router B
Stacked Switch
Stacked Switch
DC Router A
DC Router B
Legacy Ethernet + IP
  HW redundancy: two of everything
  First Hop Redundancy: VRRP
  Redundant connections to the IP Network
  No Spanning Tree
Limitations
  Servers are multihomed  no LACP
  Poor link utilization (no active/active scenario)
  BUM & Mac learning problems due to the topology
  InterDC VLAN stretch without redundancy (L2 VPNs)
  Mixed mode stacking not so problem free

## Slide 6
Previous Architectures: (closed) Fabric architectures
6
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
Limitations:
  Complex implementations often problematic in large scale
  Difficulty in debugging due to ‘closed’ proprietary solutions
  Often platforms are immature which results to bugs
  Eventually too many hours wasted in troubleshooting and bringing the solution to ‘production ready’ state.
  All tested solutions already outdated
  Looking for something new to avoid vendor ‘black box’ solutions
Core Router A
Core Router B
Linecard switch
Linecard switch
Aggregation Switch
Aggregation Switch
LACP
LACP
Link for multi-chassis synchronization

## Slide 7
IP Fabric (aka IP Clos): the recipe
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
7
Overlay Networking with EVPN as control plane
  In theory decouple the network from the physical hardware  programmatically provisioned in a much larger scale
  All_active physical topologies
  Anycast layer 3 gateways
All traffic is L3 with: VXLAN
  Dataplane encapsulation for Overlay Tunnels
  Limitations: network overhead since all VM traffic is now encapsulated with VXLAN header (+64 bits)
No STP / no MC-LAG
Topology:
  Build a decades old topology  IP Clos
  Make use of existing hardware  Juniper QFX5K as ToR switches
  Add two new powerhouse Devices for the spine layer  Juniper QFX10K
Notes: 7

## Slide 8
VXLAN: Brief introduction
RFC 7348
Tunneling (overlay) protocol that encapsulates all traffic in IP/UDP
Can be described as MAC-over-UDP with a globally unique identifier
  VLAN-like separation, according to VXLAN ID
Tunnels are build between VXLAN Tunnel Endpoints (VTEPs)
Need of a control plane to minimize flooding and better facilitate learning
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
8
Overview
Payload
VXLAN VNID
Outer IP
Forward traffic between IP Fabric nodes referred to as the underlay
Service Separation
All traffic is L3 no need for STP

## Slide 9
EVPN: Brief introduction
RFC 7432: BGP MPLS-Based Ethernet VPN
  Co-authored by Cisco,Juniper, Alcatel-Lucent, Verizon, AT&T
Stated as evolution over existing L2VPN and VPLS solutions
Can use both MPLS and VXLAN as transport
Solves flood and learn problem mentioned in VXLAN
Provides redundant (anycast) gateways
Active / Active server multihoming
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
9
Overview
Implemented as another BGP address family (NLRI)
Introduces Route Types for
  Ethernet Segment (ES) Auto discovery
  MAC/IP advertisement
    MAC addresses are treated as routable addresses and advertised via BGP
  BUM traffic and loop avoidance
  PE devices in same ES auto discovery (allows for active/active)
Traffic is sent to the appropriate VTEP (no flooding)
Route filtering & route distribution
Key Concepts

## Slide 10
GRNET IP Fabric topology
10
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
Spine & Leaf topology
SPINE: Juniper QFX1002
  nx10G uplink to GRNET core
LEAF: Juniper QFX5100
  2x40G uplink
Server:
  2x1/10G UTP
    Multihoming: In pairs of racks
  LACP or Active-Backup
Core Router A
Core Router B
Juniper QFX5K
Juniper QFX5K
Juniper QFX10K
Juniper QFX 10K
Juniper QFX5K
Juniper QFX5K

## Slide 11
The Underlay Network
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
65491
65492
65401
65402
65403
65404
11
Each IP Fabric device acts as L3
eBGP between the devices:
  Route distribution of Loopbacks
  Multipath load balancing between available paths
Loopbacks & Backbone links from 10.0.0.0/8
One Private AS per device
Unique assignments within GRNET (for future inter-DC connectivity)
Loopback IPs & ASN helps to identify rack number
Loopbacks are used as VXLAN VTEPs (Tunneling Endpoints)

## Slide 12
The Overlay Network
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
65499
65499
65499
65499
65499
65499
12
iBGP mesh among all devices
  Additional AS# for iBGP
  Spines: route reflectors
  EVPN address family (nlri)
EVPN: Advertise MACs (…)
  Each PE advertises its local MACs (per VXLAN)
  L3 devices advertise MAC-IP bindings (per VXLAN)
L3 (gateways)@Spines
  Mostly because of limitations of the leaves (QFX5100).
  Distributed Gateway for redundancy and performance
Server ports
  Trunk or access
  VLAN <-> VXLAN
  LACP with two PE devices + loop avoidance

## Slide 13
L2 stretch between Datacenters
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
13
Customer data routing is done at the Spines
Data Center interconnect using ‘Asymmetric routing’  Egress PE does only L2 lookup to the local ethernet switching table that is populated from the EVPN control-plane
Spines are connected over eBGP underlay to announce the VXLAN termination points (IPs used for the overlay network)
Spines are connected over iBGP overlay to announce the MAC+IP NLRIs (EVPN)
Ingress
MAC-VRF IP-VRF
Egress
IP-VRF MAC-VRF
1
2
3
4
5
MAC REWRITE

## Slide 14
Automation
Describe the topology with the addressing scheme in one YAML file
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
14

## Slide 15
Ansible and IP Fabric
New roles (templates + tasks) to our Ansible playbooks
  dcf-topology
  dcf-service
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
Allow new tasks to be executed and build underlay/overlay topologies
15

## Slide 16
Introduce a new service
Build server interfaces, VLANs and Layer 3 redundant gateways via Ansible
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
16

## Slide 17
Compete playbook run
17
Build one complete IP Fabric DC configuration and deploy L2 and L3 services in under 3 minutes!
  In this example Ansible has produced configuration for 36 Leaves and 2 Spine switches with 597 interfaces and 377 VLANs (!!!)
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters

## Slide 18
Reality: An adventure
Addressing scheme for
  VTEP IPs
  IN-band management -> loopbacks
    Eventually a new carrier VRF to completely separate the management traffic
  Underlay ASNs
  Multiply by number of DCs
Many limitations on the Broadcom chipset on QFX5100
Early adoption of EVPN implementation on QFX platforms
  Bugs…
Easier troubleshooting due to openness of the solution
Lot of support/attention from Juniper (win-win case)
Netconf support from the beginning: ease of service deployment and configuration changes with Ansible
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
18

## Slide 19
Thank you!
13 Jun 2018, TNC18, Trondheim
IP Fabric solution for GRNET Datacenters
19