## Slide 1
Guy Roberts, Sebastiano Buscaglione, Mian Usman
GÉANT Network Evolution
Trondheim
12 June 2018

## Slide 2: Building a new network
RFI
Regional
Studies
Financial
Modelling
Platform
Evolution
CTO
Workshops
& approval
Challenges:
Traffic growth/cost control
GN4-3 IRU
Infrastructure sharing
Notes: July 2017 - regional studies established to define regional needs and gathering local intelligence
First CTO workshop Nov 2017
An additional regional study for central Europe
Large RFP to market for connectivity (525 quotes / 35 providers)
Built financial model for traffic forecasting and analyse cost impact of options
Regional studies meeting in Rome to consolidate topology
Second CTO workshop May 2018
Governance review and ratification

## Slide 3: GÉANT network architects
Guy Roberts
Regional Studies
Sebastiano Buscaglione
Planning the Network Topology
Mian Usman
Platform Evolution
Notes: Three network architects in GÉANT
They have developed the network evolution strategy

## Slide 4
Regional Studies
GÉANT Network Evolution
Guy Roberts
Trondheim
12 June 2018

## Slide 5: Scoping a new network – the process
RFI
Regional
Studies
Financial
Modelling
Platform
Design
CTO
Workshops
& approval

## Slide 6: Regional studies - objectives
Preparation for next network, began 12 months ago. Fibre contracts expire in 2020
Network topology – fibre and circuits
Survey users and network capacity requirements
Review existing infrastructure and potential to share NREN fibre
Pricing intelligence
Regional Study reports & consolidation
Notes: Existing infrastructure
  Review of GÉANT topology and PoPs
  Review of existing NREN infrastructure
  Review of commercial fibre availability in the region
Cost Analysis
  Intelligence in the local region
  Moving to more infrastructure sharing with NRENs
  Collect offers from NRENs and commercial providers

## Slide 7: Five regional studies
7
Ireland
UK
UK/Ireland
Led by Guy Roberts
Belarus
Latvia
Estonia
Lithuania
Russia
Finland
Sweden
Norway
Denmark
Baltic - Led by Ieva Muraškienė
Poland
Greece
Hungary
Bulgaria
Romania
Serbia
South East Europe - Led by Pavel Skoda
Albania
Slovakia
Israel
Cyprus
Turkey
Macedonia
Montenegro
Croatia
France
Croatia
Central Europe region - Led by Sebastiano Buscaglione
Poland
Germany
Italy
Switzerland
Austria
Czech
Republic
Slovenia
Malta
Holland
Belgium
UK
Spain
Hungary
Luxembourg
+ Nordunet
Portugal
Spain
Iberian Peninsula
Led by Emanuel Massano
France

## Slide 8: UK/Ireland - Current
Western dark fibre ring passes through London
Two PoPs in London with extension link to Jisc
2 x 100G leased circuits to Dublin
Two PoPs in Dublin
Notes: Existing connectivity:
Western dark fibre ring passes through London
Two main Pops in London with extension link to Jisc
2 x 100G leased circuits to Dublin
Two PoPs in Dublin

## Slide 9: UK/Ireland – Challenges
Challenges
Meet growth for 15 years
Remove London shared risk
100G transatlantic circuit landing in Dublin
Second Ireland PoP outside Dublin
Meet GÉANT core from another UK city
More subsea diversity
Solutions
IRU on subsea system will support London bottleneck bypass
Manchester PoP and third link out of UK

## Slide 10: UK/Ireland – Proposal
Subsea bypass of UK
Make use of UK fibre in future
Third link out of UK
Notes: Lon-Dub route uses Jisc spectrum and proposes moving second UK PoP to Manchester
Aqua Comms link used for third link to Europe
Requires a collaboration after 2023 to updated Manchester-Dublin fibre
Reserve some IRU contingency for this

## Slide 11: Iberian Peninsula – Current
Dark fibre extends to Madrid
100Gbps to Paris, 20Gbps to London
Each PoP has two links back to dark fibre core
Dark Fibre
100 Gbps leased circuits
20 Gbps leased circuits
20 Gbps CBF from NRENs
LIS-Lisbon, MAD-Madrid, PAR-Paris MAR-Marseille, LON-London
MAD
LON
PAR
MAR
LIS
LIS
Notes: Current dark fibre footprint extends to Spain (Madrid – Marseille)
100Gbps link to Paris
20Gbps link to London
Each PoP has two links back to a GÉANT dark fibre PoP

## Slide 12: Iberian Peninsula – Challenges
Challenges
No fibre to Portugal
Long-line to fibre core -> poor latency
Need connectivity for BELLA
Solutions
Fibre IRU will support growth and services
Fibre ring for in region will remove long-line back to fibre core for smaller NREN
Link BELLA landing station on fibre will allow capacity expansion

## Slide 13
Iberian Peninsula – Proposal
Establish an Iberian ring with fibre to Portugal
New PoP in Bilbao, move PoP to Porto or Sines
Results in improved resiliency/latency
Support BELLA traffic
MAD
BIL
PAR
MAR
POR
LIS
SIN
LIS-Lisbon, MAD-Madrid, PAR-Paris MAR-Marseille, LON-London
Dark Fibre
100 Gbps managed service
NREN CBF

## Slide 14
Dark fibre in Croatia, Slovenia and Hungary
20Gbps leased ring to Athens
20Gbps ring to Bulgaria and Romania
‘off-net’ PoPs has two links back to a GÉANT dark fibre PoP where possible
South East Europe - Current

## Slide 15: South East Europe - Challenges
Challenges
Many large countries not on dark fibre
Remove hub-and-spoke architecture
Use NREN spectrum
Solutions
Dark fibre allows for traffic growth, and GÉANT Lambda service
Allows small to be connected to nearby country
Mesh of architecture will reduce latency
Reduced cost

## Slide 16
SE Europe - Proposal
Notes: Ring to Athens
Ring allows Macedonia, Montenegro and Albania to be connected locally
Improved latency for local traffic
Spectrum on GARR, GRNET, NIIF, AMRES, RoEduNet

## Slide 17: Baltics – Current
Dark Fibre
NREN operated leased circuits
Leased circuits
Ring with 2x10G
Commercial and NREN circuits
TAL-Tallinn, TSIR-Tsirguliina, RIG-Riga, SIAU-Siauliai, KAU-Kaunas, POZ-Poznan, FRA-Frankfurt, HAM-Hamburg, HEL-Helsinki, AMS-Amsterdam, LON-London, GEN-Geneva, PRA-Prague

## Slide 18: Baltics – Challenges
Challenges
Traffic growth
Lack GÉANT lambda services
Solutions
IRU will support growth and services
Fibre ring

## Slide 19: Baltics - proposal
TAL-Tallinn, TSIR-Tsirguliina, RIG-Riga, SIAU-Siauliai, KAU-Kaunas, POZ-Poznan, FRA-Frankfurt, HAM-Hamburg, HEL-Helsinki, AMS-Amsterdam, LON-London, GEN-Geneva, PRA-Prague
Notes: Objective: to close the Baltic Ring with NREN fibre where possible
Fibre based services available all through the region
Spectrum offers available from NORDUNET, PSNC, LITNET, EENET

## Slide 20: Central European - Proposal
More fibre sharing.
Shortcut through Brussels on Amsterdam – Paris to form two smaller rings. Reducing latency and improving re-routing.
Smaller sites on Eastern ring moved out of the Central ring to be connected via Eastern European fibre infrastructure.
Luxembourg still connected via lease capacity, but fibre sharing explored. Included potential Paris – Frankfurt shortcut.

## Slide 21: Summary
Five studies carried out
Each have reported the requirements for their region
These are being used as inputs to the network design
Local expertise key to good solution
Full results available in reports