## Slide 1
Phaethon: a lightpath provisioning adapter for LightSoft
Charalampos Andreou
June 2018

## Slide 2
OCh and LightPath
OTN
Transponder
Filter
Reconfigurable Optical Add-Drop Multiplexer

## Slide 3
Lightpaths in the GRNET OSS/BSS stack

## Slide 4
Lightpaths in the GRNET OSS/BSS stack
Phaethon

## Slide 5
Provisioning sequence diagram

## Slide 6
Phaethon
Adapter of the MTNM TMF-814 (NorthBound Interface) for LightSoft
Direct transformation of CORBA calls to HTTP Rest calls (JSON payload)
Complex requests - Operations extension (Phaethon manager)
Notification service

## Slide 7
getAllSubnetworkConnections: Retrieval of all SNCs of all subnetworks
getAllSubnetworkConnectionsWithTp: Retrieval of all SNCs that use specific termination points
getRoute: Retrieval routes for a specific SNC
getSubnetworkConnection: Retrieval of SNC with all associated details)
Connection Retrieval
API Direct Requests (MTOSI v4.0)
getAllEquipment: Retrieval of the equipment included in a managed element
getAllSupportingEquipment: Retrieval of equipment with PTP/FTP ή Matrix Flow Domain
getEquipment: Retrieval of details of equipment
Equipment Retrieval
getAllManagedElements: Retrieval of all managed Managed Elements under control of a specific ManagedElementMgr
getManagedElement: Retrieval of Managed Element with details
Managed Element
getContainingMultiLayerSubnetworkNames: Retrieve all names of MultiLayerSubnetwork
getContainingMultiLayerSubnetwork: Retrieve all MultiLayerSubnetworks
getAllTopLevelMultiLayerSubnetworks: - Retrieve all top level MultiLayerSubnetworks
Multilayer Subnetwork Retrieval
getAllEdgePoints: Retrieve all Edge points – Termination points that are able to undertake a connection
getTerminationPoint: Retrieve a Termination point in detail.
getContainedCurrentTPNames: Created to managed produced exceptions (not served by the Corba server)
getContainedPotentialTPNames: Created to managed produced exceptions (not served by the Corba server)
Termination Point Retrieval
getAllTopLevelTopologicalLinks
getAllTopologicalLinks: Retrieve all topological links in the NMS.
getTopLevelTopologicalLink: Retrieve details of Topological Link
Topological Link Retrieval
setTerminationPointData: Modify the parameters of a termination point (Termination Point, CTP, PTP or FTP). Best effort process.
Termination Point Control

## Slide 8
API Update Delete (MTOSI v4.0)
setTerminationPointData: Modify the parameters of a termination point (Termination Point, CTP, PTP or FTP). Best effort process.
Termination Point Control
createTopologicalLink: Creation of a Topological Link
deleteTopologicalLink: Deletion of a Topological Link
Topological Link Control

## Slide 9
API Ph_Managers calls
Termination Point Retrieval
getAllConnectionlessPortTerminationPoints
getAllConnectionlessPortTerminationPointsForME
Managed Elements
All TPs
All Subnetwork Connections
Route
Route Endpoints
CrossConnections (aEnds-zEnds)
LSNExt_SpeificClientType is
ODU2, ODU2E,
10GbE, 100GbE
LSNExt_LEUnit contains TR (Transponder)
Termination Point name contains UME
All Termination Points
Used Termination Points

## Slide 10
API Ph_Managers calls
checkValidSubnetworkConnection
createAndActivateSubnetworkConnection
deactivateAndDeleteSubnetworkConnection
createAndActivateSubnetworkConnectionAtOnce
deactivateAndDeleteSubnetworkConnectionAtOnce
Connection Control
Endpoint Compatibility Check (TunedFrequency, LSNExt_TunedFrequencyRx, LSNExt_FECOverhead, LSNExt_SpecificClientType)
checkValidSNC
Endpoint Compatibility Check
Endpoint Correction
createAndActivateSNC

## Slide 11
CORBA server exceptions
ProcessingFailureException (TMF 814)
Ph_ProcessingFailureException to analyze the exception towards Phaethon
IOEcxeption and UserException
Exception handling
String message | 
NOT IMPLEMENTED | 0
INTERNAL ERROR | 1
INVALID INPUT | 2
OBJECT IN USE | 3
INVALID ENDPOINT | 4
ENTITY NOT FOUND | 5
TIMESLOT IN USE | 6
PROTECTION EFFORT NOT MET | 7
NOT IN VALID STATE | 8
UNABLE TO COMPLY | 9
NE COMMUNICATION LOSS | 10
CAPACITY EXCEEDED | 11
ACCESS DENIED | 12
TOO MANY OPEN ITERATORS | 13
UNSUPPORTED ROUTING CONSTRAINTS | 14
USER LABEL IN USE | 15
DEFAULT UNMAPPED EXCEPTION | 16

## Slide 12
Internal Phaethon exceptions
TPCompatibilityException as a results of checkValidSNC or createAndActivateSNC
Ph_MultiLayerSubnetworkException during the retrieval or creation of the SNC
RestExceptionHandler (towards BSS)
Exception handling
String message | 
TunedFrequency | 0
LSNExt_TunedFrequencyRx | 1
LSNExt_SpecificClientType | 2
LSNExt_PortType | 3
DifferentProvisioning | 4
LSNExt_FECOverhead | 5
Unknown Exception | 6
String message | 
OCh Trail Not Found | 0
LP Trail Not Found | 1
Failed Deactivate And Delete SNC for LP | 2
Failed Deactivate And Delete SNC for OCh | 3
Subnewtwork Connection Retrival Failure | 4
Unknown Exception | 5

## Slide 13
Notifications
NOTIFICATION_MODE
MANUAL_MODE, based on logical expressions
  Configuration based on “alarming.properties”
  Example
    $type_name == 'NT_ALARM' and $filterable_data(perceivedSeverity) == 5
      PS_INDETERMINATE = 0 , PS_CRITICAL = 1, PS_MAJOR = 2, PS_MINOR = 3, PS_WARNING = 4, PS_CLEARED = 5;
    $filterable_data(perceivedSeverity) <= 3

## Slide 14
LightApp example: OCh related End points
How to get OCH related End points for some NE identified by its DN
HTTP command: GET
Type of service execution: Asynchronous
URI example of synchronous execution
http://pogs:7001/LightApp/resources/topology/v1/OCH/endpoints?servicecategory=ECI_OCH&portrate=all&endpointstatus=available&neid=EMS~~ECI/EMS_STMS_9@@ManagedElement~~151
Main query parameters description: portrate, serviceType, directionality, endpointstatus
Example of operation execution output:
{"EMS~~ECI/EMS_STMS_9@@ManagedElement~~151": [2]
0:{
"element": "OTU2e-u2/3"
"slot": "Slot u2 (TR10_4)"
"port": "OTU2e-u2/3"
"numberOfTunableFrequencies": 88
"frequencySpacing": "DWDM_50"
"wdmMode": "DWDM"
"txChannelFrequency": 192.2
"rxChannelFrequency": 192.2
"supportedFEC": "FEC"
"tunable": true
"dn": "EMS~~ECI/EMS_STMS_9@@ManagedElement~~151@@PTP~~port-u2/3"
"rate": "OTU2"
}
Possible values of frequencySpacing
CWDM
DWDM_50
DWDM_100
DWDM_1000
Possible values of wdmMode
CWDM
DWDM

## Slide 15
Thank you
bcand@di.uoa.gr

## Slide 16: Automated Service creation between NREN Domains
Jonathan Homa
Director, Portfolio Marketing
TNC18, Trondheim, June 2018

## Slide 17: Local service orchestration
  Starting point:
  You have successfully implemented SDN+NFV service orchestration within your NREN domain
  You can now bring up new services in minutes, like E-line service shown
Business and Service Orchestration
E-line service

## Slide 18: challenge
  How do you extend this service creation agility between NREN domains
  Any-to-any connectivity
    Rapidly
    Even for short duration use

## Slide 19: Physical Connectivity not an issue
  Leveraging GEANT’s network (in Europe at least)
  But still need to orchestrate services between NREN domains

## Slide 20: Inter-NREN Service orchestration
Orchestrated E2E E-Line Service
ENNI
ENNI
UNI
UNI
NREN 1
NREN 2
Business and Service Orchestration
Business and Service Orchestration
Business and Service Orchestration

## Slide 21: MEF 3.0 solution framework
Chart: 
| Services | Certification | Community | 4th Qtr
Sales | 0.25 | 0.25 | 0.25 | 0.25
LSO APIs
Services
Community
Certification
    The MEF 3.0 Services Framework
    A traditional services framework
    Defining, delivering, and certifying agile, assured, and orchestrated services
    Across a global ecosystem of automated networks
    Was launched in November 2017

## Slide 22: MEF 3.0 Lifecycle service orchestration (LSO) Reference Architecture
Network Infrastructure
CANTATA
(CUS:BUS)
ALEGRO
(CUS:SOF)
SONATA
(BUS:BUS)
INTERLUDE
(SOF:SOF)
Customer
Application
Coordinator
LEGATO
(BUS:SOF)
PRESTO
(SOF:ICM)
ADAGIO
(ICM:ECM)
Business Applications
Service Orchestration Functionality
Infrastructure Control and Management
Element Control and Management
SP #1 Domain
Customer Domain
LEGATO
(BUS:SOF)
PRESTO
(SOF:ICM)
ADAGIO
(ICM:ECM)
Business Applications
Service Orchestration Functionality
Infrastructure Control and Management
Element Control and Management
Network Infrastructure
ENNI
    CUS: Customer Application Coordinator
    BUS: Business Application
    SOF: Service Orchestration Functionality
    ICM: Infrastructure Control and Management
    ECM: Element Control and Management
SP #2 Domain

## Slide 23: ECI LSO Innovation platform
A subset of ECI’s Muse commercial PaaS, which provides a distributed cloud-native development and deployment environment for microservices applications
Plus microservices for the Sonata, Interlude and Presto interfaces

## Slide 24: MEFNET: building “LSO use cases”
ECI
LSO Innovation Platform

## Slide 25
MEF 3.0 service fulfilment & activation (SF&A) implementation project
Reduce fulfilment and activation of a MEF 3.0 service spanning multiple operator domains
from
months
to
minutes

## Slide 26: WHERE ECI FITS
SF&A project
Phase 1
Hong Kong to NJ
Phase 2
NJ to South Africa and NJ to Uganda
Service Orchestration in each of the 5 operator domains to orchestrate an IP ‘service’ lifecycle

## Slide 27: Can also be used to connect NRENS
ENNI
ENNI
UNI
UNI
NREN 1
NREN 2
Business and Service Orchestration
Business and Service Orchestration
Business and Service Orchestration
LSO Innovation Platform
ECI
ECI’s LSO Innovation Platform, working through MEF, provides an ideal tool to explore automated service connectivity between NREN domains
Orchestrated E2E E-Line Service

## Slide 28: Thank YOU!
Please be sure to stop by booth #14 for further discussion.