## Slide 1: AmLight’s SDN Looking Glass – An SDN centralized monitoring system
Jeronimo Bezerra <jab@amlight.net> Florida International University
TNC, June 12th 2018
Antonio Francisco <antonio@amlight.net>
Academic Network at São Paulo

## Slide 2: AmLight: a Distributed Academic Exchange Point
Production SDN Infrastructure since Aug-2014
NAPs: Miami, Brazil(2), Chile, and Panama
Multiple 10G and 100G links
Carries Academic and Commercial traffic
Control Plane: OpenFlow 1.0 and 1.3
Network Programmability/Slicing
Inter-domain Provisioning with NSI
2000+ R&E institutions connected
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 3
SDN vs. Troubleshooting
Why troubleshooting a SDN network is so complex?
OpenFlow has minimum support for troubleshooting
  For instance, there are no special/reserved flow cookies
Current SDN applications only consider network provisioning
  Need for troubleshooting features only appears once things start falling apart
Many academic papers suggesting solutions that do not fit in production
  Highly dependent on the controller for actions
  Heuristic and Machine Learning per unknown packet do not scale
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 4
SDN vs. Troubleshooting (2)
SDN concept itself makes things harder sometimes
  Because datapaths have no intelligence at all, controllers always have to be involved
    Creating scalability and timing issues
    Making controllers more complex to operate and maintain
Lack of support from vendors for useful OpenFlow features
  Counters are not trustworthy, action OFPP_Table is not supported, ...
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 5
Our 2016/2017 Vision
A single side-application for troubleshooting made sense:
  Pros:
    Frees the provisioning developers to focus on provisioning
    Avoids duplicated data when multiple SDN applications are running in production
    Eases auditing
    Centralizes all troubleshooting data, making it easier to correlate events
      OpenFlow agent, NMS, SDN app, slicer and sniffer’s data are processed by just one entity
  Cons:
    Running OpenFlow applications in parallel is still a challenge:
      ONOS deletes unrecognized flows, which makes design with other third parties controllers inviable.
      OpenFlow roles and multiple Masters: multiple masters ack as standalone controllers and just a few controllers actually support all role modes (SLAVE, MASTER, NONE)
    No East-West protocol standardized
      Each SDN app will have to be customized to gather status and counters from a remote app
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 6
Our 2017/2018 Vision
A set of single micro-applications over the same framework makes more sense:
Pros:
  Frees the provisioning developers to focus on provisioning
  Avoids duplicated data when multiple SDN applications are running in production
  Eases auditing
  Centralizes all troubleshooting data, making it easier to correlate events
    OpenFlow agent, NMS, SDN app, slicer and sniffer’s data are processed by just one entity
  No conflicts when running OpenFlow controllers in parallel
  Easy integration with production applications in the same framework (Kytos, ONOS, ODL, etc.)
Cons:
  OpenFlow controller-dependent solution:
    Kytos Napps only work with Kytos SDN controller, and ONOS apps only work with ONOS SDN controller
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 7
Original
Previous
Current

## Slide 8
AmLight SDN Looking Glass
Central point for SDN monitoring:
  Centralizes all monitoring and troubleshooting information being slice/app-independent
  Stores all statistical data (flow, ports, etc.) and OpenFlow messages into a persistent backend
  Tracks real time OpenFlow control plane messages
  Takes network snapshots: save the network state for future troubleshooting and capacity planning
Central point for SDN troubleshooting:
  Runs trace paths (”traceroute”) in both Data Plane and Control Plane
  Sends alerts via e-mail and Slack
  Provide REST to be used by external SDN apps, auditing tools, and external NMS
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 9: AmLight SDN Looking Glass - Components
The AmLight SDN Looking Glass is composed of the following Napps:
  Stats: Gets flow stats from switches and store them.
  Sniffer: Monitors the Control Plane
  SDNTrace CP: Traces a path using flows acquired by the Stats app
  SDNTrace DP: Data Plane path tracing
  Notifications: Sends notifications when problems occur
  Topology: Discovers topology
  Web UI for network visualization
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 10
AmLight SDN Looking Glass
Developed in Python 3.6
Built as a series of Napps on top of Kytos SDN framework
Uses Influxdb and Kytos/StoreHouse for persistence
Uses Grafana and JavaScript D3 for visualization
Supports both OpenFlow 1.0 and OpenFlow 1.3
Integrates with the AmLight OpenFlow Sniffer
Open Source/GPL
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 11
AmLight SDN Looking Glass Software Stacks
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018
Controller:
Web:
DB:
Messaging:
{RESTful API}

## Slide 12
Topology Discovery
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 13
Switch info
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018
Notes: update screenshots

## Slide 14
Flow Table
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018
Notes: We have a REST endpoint returning the flows installed in a switch at a certain datetime. The web view is not ready yet, but the look will be similar to this.

## Slide 15
Tracing Paths
Control Plane: uses flow entries collected through OFP_STATS_REQUEST
Data Plane: sends Ethernet probes to match user flow entries (via OFPP_TABLE action)
Manual tests are supported:
  The SDN LG always compares the Control Plane results ("correct" path) with the Data Plane results ("actual" path detected).
  In case CP and DP results are different, a notification is send to Admins
Scheduled routine run CP path traces at every interval and randomly sample some circuits to test in the Data Plane:
  Reason is to avoid overloading the switches' CPU
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 16
Trace Path Form
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 17
Trace Path
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 18
Notes: Error: Flow Space Firewall rejecting FLOW MODs

## Slide 19: SDN Looking Glass Compatibility
Evaluated OpenFlow Switches:
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018
Switch Platform | Firmware Version | OpenFlow version | Control Plane Tracing | Data Plane Tracing | Topology Discovery | Flow Stats
OvS | 2.9.0 | 1.3 | SUPPORTED | SUPPORTED | SUPPORTED | SUPPORTED
Dell Z9100-ON | 9.11(0.0P6) | 1.3 | SUPPORTED | NOT SUPPORTED | SUPPORTED | SUPPORTED
Corsa DP 2400 | 3.0.2 build 12 | 1.3 | SUPPORTED | NOT SUPPORTED | SUPPORTED | SUPPORTED
Brocade MLXe | 6.2.0b T177 | 1.3 | SUPPORTED | NOT SUPPORTED | SUPPORTED | SUPPORTED

## Slide 20: SDN Looking Glass Deployment
Two installation methods:
  Single server with all components (complex how-to)
  Docker containers:
    Kytos
    InfluxDB
    Grafana
    ofp_sniffer
GitHub: https://github.com/amlight/sdn-lg
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 21: Future
Next Steps:
  Monitoring OpenFlow Meters
  Monitor Interface Queue utilization
  Use SNMP to monitor CPU and memory utilization
  Network configuration snapshots
    Save the network state (flows, CPU/memory, topology, link status, last OF messages exchanged, etc.) for future troubleshooting
  Small functionalities:
    Work in fully passive mode (for parallel OF controller scenarios)
    "Discover" topology through other approaches (file, API, etc.)
AmLight’s SDN Looking Glass - An SDN centralized monitoring system – TNC 2018

## Slide 22: THANK YOU!
Antonio Francisco <antonio@amlight.net>
Academic Network at São Paulo
Jeronimo Bezerra <jab@amlight.net> Florida International University
AmLight’s SDN Looking Glass - Central monitoring system for SDN
TNC 2018
Rogerio Motitsuki
<rogerio@amlight.net>
Academic Network at São Paulo
Vinicius Arcanjo
<vinicius@amlight.net>
Rede Nacional de Ensino e Pesquisa